## Slide 1
Lecture 6: Visible Light Communication

## Slide 2: Outline
Part 1
  VLC introduction
  LED introduction
  VLC potential application
Part 2
  VLC components
  Technical challenges

## Slide 3: VLC introduction
VLC (Visible Light Communication)
: New communication technology using “Visible Light”.
Visible Light
: Wavelength between ~400nm (750THz，purple) and ~700nm (428THz，red)

## Slide 4: VLC introduction （2）
General Characteristic
  Visibility : Aesthetically pleasing (美观)
  Security : What You See Is What You Send.
  Health : Harmless for human body and electronic devices
  Unregulated : no room to use more radio frequency（无管制）
  Using in the restricted area : aircraft, spaceship, hospital
  Eye safety

## Slide 5
1900s
Current
400 B.C.
1800s
280 B.C.
1880
~
Fire
Sunlight
Lamp
LED
Heliograph
（日光反射器）
Beacon
Fire
（烽火台）
Pharos
Lighthouse
（法罗斯灯塔）
Ship-to-ship
Comm.
Photophone
By Bell
Traffic Light
/Signboard Light
800 B.C.
Burning Kite
In Battle
VLC history
VLC

## Slide 6
Information delivery through reflection by mirror (Heliograph，日光反射器)
The use of fire or lamp
  Beacon fire(烽火台), Pharos lighthouse(法罗斯灯塔), ship-to-ship comm. by Morse code (1800s)
Traffic light : signal discrimination by color (Walk/Stop)
Morse
code
VLC history – Low speed
Notes: 斯巴达300勇士 法罗斯灯塔：在法罗斯岛上矗立着被称为古代世界七大奇观之一的灯，280 B.C. 摩斯密码编码简单清晰，二义性小，编码主要是由两个字符表示："."、"-"，一长一短
1912年，著名的泰坦尼克号游轮首航遇险时，发送的是CQD（英国马可尼无线电公司决定用CQD作为船舶遇难信号），但因D（—··）易于其他字母混淆，周围船只并未意识到是求救信号，没有快速救援，在快沉没时才使用的新求救信号SOS（···———···）发报。泰坦尼克号沉没后，SOS才被广泛接受和使用。

## Slide 7
Bell’s Photophone (光电话，1880)
  Optical source : sunlight
  Externally modulation by vibrating mirror (振动镜外调制)
  Receiver : parabolic mirror with crystalline selenium cells (带有结晶硒网格的抛物面镜)
  700 ft (213m) sound transmission
VLC history - Photophone
Excerpted from: The New Idea Self-Instructor edited by Ferdinand Ellsworth Cary, A. M. (Monarch Book Company, Chicago & Philadelphia, 1904)
http://www.freespaceoptic.com/
Notes: 1880年，Alexander Graham Bell和他的助手Sumner Tainter公布了光通信技术的巨大进步，他们称之为“光电话”。没有激光或现代检测器的帮助，光电话可以在数百米的光束上传输人类声音。光电话是世界上第一个光电系统，贝尔和泰纳的实验至少比无线电进行无线语音通信早了19年。

## Slide 8
Low Frequency
(Long wavelength)
Coverage
Mobility
visible
IR
UV
700nm
400nm
100μm
RF
3cm
1m
1nm
428THz
750THz
3THz
10GHz
300MHz
300PHz
High Frequency
(Short wavelength)
Bandwidth
Security
1mm
300GHz
IrDA
802.15.3c
(个域网)
IG-THz
IG-VLC
802.11(局域网)
802.16（城域网）
IG-THz : contribution 15-07-0623-01, AT&T Labs discussed the Terahertz spectrum band
which covers 300 GHz to 10 THz.
This mmWave WPAN will operate in the new and clear band including 57-64 GHz unlicensed band
The millimeter-wave WPAN will allow high coexistence (close physical spacing)
with all other microwave systems in the 802.15 family of WPANs
Frequency band for VLC
Notes: Terahertz Interest Group (IGthz) ：2012年日本东京工业大学预测利用太赫兹通信技术进行无线数据传输的速度，理论上可以高达每秒100千兆位。
IrDA是红外数据组织（Infrared Data Association），到目前为止，全球采用IrDA技术的设备超过了5000万部。初始的IrDA1.0标准制订了一个串行，半双工的同步系统，传输速率为2400bps到115200bps，传输范围1m，最近IrDA扩展了其物理层规格使数据传输率提升到4Mbps。

## Slide 9
Data rate (bps)
115K
4M
100M
480M
16M
50M
UFIR
FIR
IR
VIR
VLC
HDR UWB
1
11
3
Distance (m)
2
6
20
50
UWB
802.11a
802.11b
Bluetooth
ZigBee
VLC Characteristic
2400
Notes: FIR为IrDA物理层标准陈废的名词，虽然如此这个名词却也常用在表示4百万位元/秒速率。 IR，VIR，FIR，UFIR都是红外技术 。 ZigBee，也称紫蜂，是一种低速短距离传输的无线网上协议，ZigBee工作在20～250kbps的速率。 IEEE 802.11，1997年，原始标准（2Mbit/s，播在2.4GHz）。 IEEE 802.11a，1999年，物理层补充（54Mbit/s，播在5GHz）。 IEEE 802.11b，1999年，物理层补充（11Mbit/s，播在2.4GHz）。

## Slide 10: VLC Characteristic
1Mb/s, 1m
100
Distance  Speed (m  Mb/s)
10
100
Power consumption
Speed
1000
50 Mb/s, 50m
500 Mb/s, 3m
4 Mb/s, 1m
10
1
Non-LOS
Interference
LOS
Security
Directivity + Simplicity
Optical connectivity saves power
(mW/Mbps)

## Slide 11
VLC vs. RF Characteristic
Property |  | VLC | RF
Bandwidth |  | Unlimited, 400nm~700nm | Regulatory, BW Limited
EMI(对外干扰) |  | No | High
Line of Sight |  | Yes | No
Standard |  | IG-VLC | Yes
Hazard(危害) |  | No | Yes (H2O reaction to 2.4GHz)
Mobile To Mobile | Visibility (Security) | Yes | No
 | Power Consumption | Relative low | Medium
 | Distance | Short | Medium
 | Power Budget | Tight | Medium
Infra to Mobile | Security | Yes | No
 | Infra | LED Illumination(照明) | Access Point
 | Mobility | Limited | Yes
 | Coverage (Distance) | Short (~10m) | Wide (Short ~ Long Range)
Notes: EMI是指电子产品工作会对周边的其他电子产品造成干扰

## Slide 12: VLC motivation
Communication community trend
  Ubiquitous (Connect each other everywhere, every time)
  Security
LED trend
  LED technology (efficiency, brightness)
  LED Cost
Environmental trend
  Health
  Energy saving
Intrinsic characteristic of VLC
  Visibility
  No interference / No regulation

## Slide 13: Outline
Part 1
  VLC introduction
  LED introduction
  VLC potential application
Part 2
  VLC components
  Technical challenges

## Slide 14: LED technical evolution
Source: Credit Suisse, 2006.11.2
Brightness / Power ratio
Cost / Brightness ratio
Incandescent
Lamp (白炽灯)
Halogen
Lamp (石英灯 )
HID
(High-Intensity Discharge,
高强度放电灯)
Fluorescent Lamp
(荧光灯)
LED
LED
LED
LED
Performance and Price comparison
2003
2005
2010
2015
50
100
150
0
1
10
100
Notes: 白炽(chi)灯
卤素灯(石英灯)：白热灯的一种，卤素灯是白炽灯的改进，它保持了白炽灯所具有的优点：简单、成本低廉、亮度容易调整和控制、显色性好（Ra=100）。同时，卤素灯克服了白炽灯的许多缺点：如使用寿命短、发光效率低（一般只有6%～10%可转化为光能，而其余部分都以热能的形式散失）。

## Slide 15
Air Pollutions(空气污染)
  UNFCCC (United Nations Framework Convention on Climate Change,联合国气候变化框架公约), Kyoto Protocol(京都议定书) to the UNFCCC
    (Dec. 1997)Decreasing CO2(10 k ton/year, 2002 at Korea)
Waste Materials & Environmental Hazards
  RoHS (Restriction of the use of Certain Hazardous Substance,限制使用某些有害物质): 1, July 2006.
    Pb(铅), Hg(汞), Cd(镉), Cr6+, Polybrominated biphenyls(PBB,多溴联苯),
    Polybrominated diphenyl eters(PBDE,多溴二苯醚)
  WEEE (Electrical and Electronic Equipment )
    Producer Responsibility
Energy saving effect
  Electricity at Korea
    278 TWh(万亿瓦时),2002, 7.2 % of USA
  20% for Lighting:55.6 TWh
  50% saving by LED:27.8TWh
  Energy Saving Effect:
    3 Nuclear Stations (1GW/day)
    2 B$/year
Source: KOPTI (The Korea Photonics Technology Institute)
LED driver

## Slide 16: LED Market Forecast
LED
DRAM
NAND
NAND, DRAM
LED
※CAGR :15%
Source: Deutsche Bank, 2007. 2
2002
2010
2006
2006
29.2
billion $
12.4
billion $
2017
LED
LED
6.3
billion $
11
billion $
29
billion $
LED market comparison with NAND, DRAM

## Slide 17: LED application
Economical
efficiency
Back Lighting
Mobile Phone
Home applications
digital device
TFT LCD TV
General Lighting
Communication
Display
General Lighting
Task Lighting(工作照明)
Signal Lamp
VLC
  Mobile to Mobile
  Infra to Mobile
Exterior, interior
display
Sign & Architecture
display
LED screen
LED
Applications
Notes: LEDs have been widely applied to back lighting, flashlamp, screen display, the signal direction and transportation means.
LED广泛应用于背光、闪光灯、屏幕显示、信号指示及交通工具等各个方面。

## Slide 18: LED modulation characteristics
R+G+B LED
B + Phosphor(磷光体) LED
RCLED
(共振腔LED)
~40 Mb/s
~100 Mb/s
~500 Mb/s
Notes: DBR（布拉格反射镜）

## Slide 19: Outline
Part 1
  VLC introduction
  LED introduction
  VLC potential application
Part 2
  VLC components
  Technical challenges

## Slide 20: VLC application
Bandwidth
Security
Coverage
Mobility
IR
UV
780nm
380nm
1nm
100μm
RF
3cm
1m
visible
Peripheral
Interface
(外围接口)
LAN
Banking
Door Lock
In Plane
Digital Hospital
ITS (Navigation)
SAMSUNG
Sign Board
e-book
Visible
LAN
RF
Prohibited
Information
Broadcast
Security
E-display
Contents
Machine

## Slide 21
Indoor application
Mobile-to-Mobile
Mobile-to-Fixed
LED Illumination Infrastructure
Mobile-to-Infra
Fixed-to-Infra
Ubiquitous
Security

## Slide 22: Requirements (Indoor application)
 | Mobile to Mobile | Mobile to Fixed | Mobile to Infra | Fixed to Infra
Link | Bi-direction | Bi-direction | Bi or Uni | Bi or Uni
Reach | ~1m | ~1m | ~3m | ~3m
Rate | ~100M | ~100M | ~10M | ~10M
Application | Contents sharing | File transfer Video streaming M-commerce(移动商务) | Indoor navigation LBS(基于位置的服务) Networked robot (网络机器人) | Data broadcast
Alternative | IrDA, Bluetooth, UWB | IrDA, Bluetooth, UWB |  | WLAN

## Slide 23: Outdoor application
Vehicle-to-Vehicle
Traffic control Infrastructure
Vehicle-to-Infra
Outdoor advertising

## Slide 24
VLC application evolution
LED penetration
Mobile
Display
Sign
ITS
Illumination
100M
Indoor
10M
Indoor
10M
Outdoor

## Slide 25: Indoor navigation scheme
 | Uni-direction | Bi-direction | Hybrid | Hot spot
Link |  |  |  | 
Rate | Down : ~10k | Down : ~10M Up : ~100M | Down : ~10k Up : ~10M | Down(light) : ~10k Down(HS) : ~100M
Infra | Lighting with optical ID | Lighting with optical ID Receiver In-building network Routing server | Lighting with optical ID RF access point In-building network Routing server | Lighting with optical ID Hot spot
Mobile | Receiver Large storage Map info Routing software | Receiver Transmitter | Receiver RF connectivity | Receiver Large storage Routing software
Other service |  | LBS Ad-hoc connection | LBS | 
Rx
TRx
Rx
Rx

## Slide 26
High-speed high-security connectivity
What You See Is What You Send
(WYSIWYS)
E-Contents Vending Machine
（电子内容物自动售货机）

## Slide 27: Demonstrations
Mobile to Mobile
(100Mbps,Samsung)
Music broadcasting
(6Mbps, Oxford Univ.)
Tx, Rx
(~30Mbps,Oxford Univ.)
Infra to Mobile
(10Mbps, Tamura Inc.)
Infra to Mobile(VLAN)
(4Mbps, Samsung)
Infra to Mobile, VLCC (Keio Univ., NEC, Toshiba, Sony, Matsushita, Casio etc. )
(4.8kbps, illuminations, visible light ID, sign board, applications based on JEITA)
Sign board
(10Mbps, Samsung)
Low
speed
High
speed
LED array
(~1Gbps, Keio Univ.（庆应义塾大学）)
Audio system
(100kbps, Hongkong Univ.)

## Slide 28
Part 1
  VLC introduction
  LED introduction
  VLC potential application
Part 2
  VLC components
  Technical challenges

## Slide 29: Overview
Visible Light Communications
  Transmitter
  Channel
  Receiver
Technical challenges
  Higher bandwidth
  Enabling mobility and reliability

## Slide 30: VLC Sources
Blue LED & Phosphor(磷光体)
  Low cost
  Phosphor limits bandwidth
  Modulation can cause colour shift
RGB triplet
  Higher cost
  Potentially higher bandwidth
  Potential for WDM (波分复用)
  Modulation without colour shift
Single chip LED spectrum
RGB LED spectrum

## Slide 31: LED Modulation
Opto-electronic response
Page 5
Measured LED small-signal bandwidth
Luxeon LED
Rs = 0.9727 
L = 33.342 nH
Cs = 2.8 nF
Cd = 2.567 nF
tt = 1.09 ns
SPICE Model

## Slide 32: Improvement of LED response
Using blue-response only (blue filtering)
Page 10
~130 ns
~25 ns
Measured optical spectrum
Measured impulse response
Issue: Only 10% of signal power is recovered
 Reducing SNR, link distance
LEDs with more blue energy [1] could be used to gain more filtered power, however the balance of white colour is shifted
Blue filtering
[1] Grubor, J., et al., "Wireless high-speed data transmission with phosphorescent white-light LEDs", Proc. ECOC 07 (PDS 3.6), pp. 1-2. ECO [06.11], 16-20 Sep. 2007, Berlin, Germany

## Slide 33: Improvement of channel response
Receiver equalisation
Page 11
Fitting falling time curve
Equalization
Measured LED impulse response
Improved LED transmission BW

## Slide 34: Channel modelling
Two propagation paths:
Line of sight (LOS): strong paths calculated using the illumination patterns from LED arrays
Diffuse (漫射): modelled by assuming the room is equivalent to an integrating sphere
Channel impulse response is calculated for each point in the room
Page 6

## Slide 35: VLC modelling

## Slide 36: Room Power Distribution
Assume
  1% modulation of typical illumination power
  Typical receiver performance
Conclusions
  Very high SNR available
    SNRmin = 38.50dB
    SNRmax = 49.41dB
  Modulation limited by source bandwidth

## Slide 37: Noise sources
Optical noise
  Daylight
    Generates DC photocurrent (光电流)
      Blocked at receiver due to AC coupling
      Creates shot noise
  Other optical sources
    Fluorescent, Incandescent (荧光,白炽)
      Creates electrical interference photocurrent harmonics
  Mitigated by
    Optical filtering
      Wavelength is in band of desired signal
    Electrical filtering

## Slide 38: Optical receiver
Receiver consists of
  Optical filter
    Rejects ‘out-of-band’ ambient illumination noise
  Lens system or concentrator (透镜系统或聚光镜)
    Collects and focuses radiation
  Photodetector (光电探测器,or array of detectors)
    Converts optical power to photocurrent
      Incoherent detection
  Preamplifier (前置放大器, or number of preamplifiers)
    Determines system noise performance
  Post-amplifier and subsequent processing

## Slide 39: Optical receiver: constant radiance theorem (常辐射定理)
Optical ‘gain’ of receiver limited by required field of view (FOV,可见区)
Wi
Wo
Ai
Ao
AiWi<=AoWo
AiWi<=Ao2p

## Slide 40: Receiver performance: figure of merit (品质因数)
Receiver Figure of Merit (FOM)
  Fibre systems
    Performance determined by sensitivity (given sufficient detector area)
    FOV usually not relevant
  Free space systems
    Etendue crucial determinant
Detector
Area
A
Receiver
sensitivity
Pmin
Field of view 2p Sr
Bit rate Rb

## Slide 41: Typical link: components
Page 22
Transmitter
16 Luxeon LEDs
PILLUM = 1.5W
LED pitch = 60 mm
IDC = 220 mA
Mod-index = 0.1
45o wide-beam lens
7 resonant freq.
Flat BW of 25 MHz
Transmitter and receiver specifications
2Rillum = 3 m
LLOS = 2 m
Receiver
Concentration lens
D = 50mm
F = 60mm
Detection area
35 mm2
Pre-Amp
Post-Amp
(ampl. limiting)
Range
L = 2 m
Rillum = 1.5 m
Rcomm = 0.5 m

## Slide 42: Typical link: illumination
Power distribution in receiving plane

## Slide 43: Typical link: BER performance
Page 23
Eye diagram
30 Mb/s
40 Mb/s
50 Mb/s
System test in normal lighting condition (room filled with other high-power white light sources)
Longer distance  SNR penalty (BER)
NRZ
Flat BW  baseline wandering reduction

## Slide 44: Bandwidth improvement: post equalisation
Pre- and post-equalization: single LED link
Pre-equalisation: experiment
Post-equalisation: simulation

## Slide 45: Retro-reflecting link (回复反射链路)
Novel optical communications between reader and tag
Low power (tag has no source)
Long range (determined by illumination source )
Visibly secure (user can see beam of light)
Notes: 44

## Slide 46: Retro-reflecting link demonstration system
Demonstrator
  2.4kb/s bi-directional communication over several metres
Notes: 45

## Slide 47: Future developments: optical MIMO
RF MIMO
Scattering provides invertible H matrix and decorrelation (capacity gain)
Difficult to shape radiation pattern with small antenna
Optical MIMO
No decorrelation
Invertible H matrix achieved by system and geometry design
Simple low-cost elements (lenses) can provide high directivity and/or complex beamshaping

## Slide 48: MIMO VLC: simulation system

## Slide 49: MIMO VLC: preliminary Results
Page 31
Position of the receiver
Aggregate data rate is linearly proportional to the number of channels and channel rate

## Slide 50: Future technical challenges
Data rate
  Equalisation
  MIMO
  Complex modulation
Integration in infrastructure
  Uplink
    Retro-reflecting link
  RF/VLC integration

## Slide 51: Homework
1. Give some application examples of VLC.
2. What are the General Characteristic of VLC?
Tips: Q1, P19; Q2, P3
5月31号交