## Slide 1: Lecture 4: Massive MIMO

## Slide 2: Contents
Introduction to Massive MIMO
Fundamental overview: Massive MIMO
Single-cell Massive MIMO
  Massive MIMO DL
    Linear precoding schemes (ZF-BF/MRT)
      Perfect CSIT / imperfect CSIT
  Massive MIMO UL
    Linear receiver techniques (ZF-R/MRC/MMSE)
      Perfect CSIR / imperfect CSIR
Multi-cell Massive MIMO
  Inter-cell interference problem
  Pilot contamination problem

## Slide 3: Introduction to Massive MIMO

## Slide 4: Introduction to Massive MIMO : Beyond 4G Network
Future mobile data traffic
  Global exponential mobile data traffic increase
    By a factor of ~ 20 from 2011 until 2016, and more expected in 2020.
  More devices, higher bit rates, always active
  Larger variety of traffic types e.g. Video, MTC
× 20
Further capacity enhancement is needed
MTC : Machine Type Communications
VoIP : Voice over Internet Protocol
M2M : Machine-to-machine

## Slide 5: Introduction to Massive MIMO : Candidate of Beyond 4G Network
Using hundreds of antennas at BS
Support the dozens of UEs
(Multi-user MIMO)
[1] RWS-120002, “Technologies for Rel-12 and Onwards,” Samsung, 3GPP RAN WS on Rel-12 and onwards, Ljubljana, Slovenia, June 11–12, 2012.
  [2] T. L. Marzetta et, “Beyond LTE: Hundreds of Base Station Antennas! “, 2010 IEEE Communication Theory Workshop
Solution for Capacity Demand[1],[2]
Massive MIMO
Benefit of Massive Antenna
  Capacity enhancement[1]
  Mathematically Exact[2]
    Required Tx energy/bit is arbitrarily small
    Eliminate the effects of uncorrelated noise & fast fading
    Compensate the poor-quality CSI
CSI : Channel State Information

## Slide 6: Introduction to Massive MIMO : Evolution of MIMO Technology

## Slide 7: Introduction to Massive MIMO
Motivation of Massive MIMO[5]
  Consider a MIMO MAC ( M : # of BSs antennas, K : # of user)
  If the BS process its receive signal by matched filtering,
  By the strong law of large numbers (大数定律),
  With an unlimited number of antennas
    Uncorrelated interference and noise vanish
    The matched filter is optimal
    The transmit power can be made arbitrarily small
: i.i.d. with zero mean and unit variance
  [5] T. L. Marzetta, “Noncooperative cellular wireless with unlimited numbers of base station antennas,” IEEE Trans. Wireless Commun., vol. 9, no. 11, pp. 3590–3600, Nov. 2010.
MAC : Multiple Access Channel
By strong law of large numbers

## Slide 8: Introduction to Massive MIMO
Simulation result
  M = 1 ~ 500, hi = M X 1 Real Gaussian Vector
Converges to 1 as M increases
Converges to 0 as M increases

## Slide 9: Introduction to Massive MIMO
On channel estimation and pilot contamination[5]
  The receiver estimates the channels based on pilot sequences.
  The # of orthogonal sequences is limited by the coherence time
  Thus, the pilot sequences must be reused
  Assume that transmitter m & j use the same pilot sequence
  Thus, the BS process its receive signal by matched filtering
  With an unlimited number of antennas
    Uncorrelated interference, noise and estimation errors vanish
    The matched filter is optimal
    The transmit power can be made arbitrarily small[6]
    The performance is limited by pilot contamination
m
m
j
pilot contamination
estimation noise
m
m
j
  [6] H. Q. Ngo, E. G. Larsson and T. L. Marzetta, “Uplink power efﬁciency of multiuser MIMO with very large antenna arrays,” in Proc. of Allerton Conference on Communication, Control, and Computing, Sept. 2011.
By strong law of large numbers
m
m
j
j
pilot contamination

## Slide 10: Introduction to Massive MIMO
Analysis of Massive MIMO with sufficient large # of BS antennas
  Single-cell massive MIMO scenario
    Massive MIMO Downlink scenario
      Analysis the performance of various linear precoding/beamforming technique for Massive MIMO based on channel information
      Perfect CSIT/ imperfect CSIT cases
    Massive MIMO Uplink scenario
      Linear receiver technique for Massive MIMO Uplink
      Perfect CSIR/ imperfect CSIR cases
  Multi-cell massive MIMO scenario
    Inter-cell interference problem
    Pilot contamination problem
CSIT : Channel State Information at the Transmitter
CSIR : Channel State Information at the Receiver

## Slide 11: Fundamental Overview: Massive MIMO

## Slide 12: Fundamental Overview: Massive MIMO : Point-to-Point MIMO (1/4)
Channel Model
  # of BS antennas M, # of UE antennas N
  IID complex-Gaussian channel H, x, n with zero mean and variance 1
  is downlink transmission power
  Receiver has perfect knowledge of H
Received SNR/ Capacity at Receiver
M>N
M<N
SNR : Signal to Noise Ratio

## Slide 13: Fundamental Overview: Massive MIMO : Point-to-Point MIMO (2/4)
Capacity at Receiver (M>N)
For large M with IID complex-Gaussian channel H,
Conclusion

## Slide 14: Fundamental Overview: Massive MIMO : Point-to-Point MIMO (3/4)
Capacity at Receiver (N>M)
For large N with IID complex-Gaussian channel H,
Conclusion

## Slide 15: Fundamental Overview: Massive MIMO : Point-to-Point MIMO (4/4)
Point-to-point MIMO
  Large number of transmit antennas
  Large number of receive antennas
Independent with M
Linearly increase as N
Increase as N with log shape

## Slide 16: Fundamental Overview: Massive MIMO : Multi-User MIMO (1/4)
Multi-user MIMO Uplink
  M antennas simultaneously serves K users
  Each user has single antenna, N = 1
  Channel modeling (large scale + small scale)
    Propagation matrix G
Massive MU-MIMO Uplink
  Only large scale fading coefficients remain
H: small scale fading
D: large scale fading (path loss, shadow fading)

## Slide 17: Fundamental Overview: Massive MIMO : Multi-User MIMO (2/4)
Massive MU-MIMO Uplink
  UL Received vector for K users
  Total capacity of UL MU-MIMO
  Detection using MRC
    SNR vector for K users
Assume Perfect CSIT
Symbol power: normalized to 1
Achievable by detection
using MRC
MRC: Maximal Ratio Combining

## Slide 18: Fundamental Overview: Massive MIMO : Multi-User MIMO (3/4)
Multi-user MIMO Downlink
  M antennas simultaneously serves K users
  Each user has single antenna, N = 1
  Channel modeling (large scale + small scale)
    Propagation matrix G
Massive MU-MIMO Downlink
  Only large scale fading coefficients remain
H: small scale fading
D: large scale fading (path loss, shadow fading)

## Slide 19: Fundamental Overview: Massive MIMO : Multi-User MIMO (4/4)
Massive MU-MIMO Downlink
  DL Received vector for BS (equal power allocation assumption)
  Total capacity of DL MU-MIMO
  Maximal Ratio Transmission (MRT) precoding based received signal
    SNR vector for K users:
Achievable by MRT
 IK

## Slide 20: Massive MIMO Downlink Channel
Deterministic Equivalent for the Achievable Sum Rate

## Slide 21: Massive MIMO Downlink Channel : System Model
Parameters
  : small scale fading
  : beamforming vector
  M : # of BS antenna
  K: # of users
  Single antenna at user
Received vector

## Slide 22: Massive MIMO Downlink Channel : Linear Precoding
Conventional linear precoding
Received signal after using linear precoding
SINR of the kth user
MRT | ZFBF
Rate of user k
Ergodic sum rate
MRT: Maximal Ratio Transmission
ZFBF: Zero-Forcing Beamforming

## Slide 23: Massive MIMO Downlink Channel : Linear Precoding – Perfect CSI
Deterministic form of the SINRk/Rsum as M, K →∞, M/K=α
  MRT
  ZFBF
SINR: Signal-to-Interference-plus-Noise Ratio
CSI: Channel State Infromation

## Slide 24: Massive MIMO Downlink Channel : Linear Precoding – Imperfect CSI
Estimated CSI ( ) using MMSE channel estimation
Deterministic form of Rsum with imperfect CSI
MRT
ZFBF

## Slide 25: Massive MIMO Downlink Channel : Linear Precoding – Simulation Results (2/2)
Ergodic sum-rate vs. M
  Simulation parameters
  Deterministic form of Rsum
    Perfect CSI, Imperfect CSI
    The approximations is very close to the numerical result
    It is also accurate even for small M, K.
  Performance comparison
    As α>>1, ZFBF > MRT
    As α=1, MRT > ZFBF
M ↑  Rsum ↑
Cross point
Channel
Imperfectness

## Slide 26: Massive MIMO Downlink Channel : Linear Precoding – Simulation Results (2/2)
Ergodic sum-rate vs. K
  Simulation parameters
  Performance comparison
    As α>>1, ZFBF > MRT
    As α=1, MRT > ZFBF
  Optimal K* for ZFBF
    ex)
MRT: K ↑  Rsum ↑
ZFBF: Concave function of K
Cross point
Optimal K*

## Slide 27: Massive MIMO Uplink Channel
Energy and Spectral Efficiency with Linear Receivers

## Slide 28: Massive MIMO Uplink Channel : Contents
Massive MIMO Uplink Channel
  System model
  Uplink power efficiency – Perfect CSI case
  Uplink power efficiency – Imperfect CSI case
  Energy efficiency and spectral efficiency tradeoff

## Slide 29: Massive MIMO Uplink Channel : System Model
Parameters
  : small scale fading
  : path loss + shadowing
  SNR for the kth UE:
Received signal

## Slide 30: Massive MIMO Uplink Channel : Linear Detector
Conventional linear detector
Received signal after using the linear detector
SINR of the kth user
MRC | ZF | MMSE
MRC: Maximal Ratio Combining
ZF: Zero-Forcing
MMSE: Minimum Mean Square Error

## Slide 31: Massive MIMO Uplink Channel : Uplink Power Efficiency – Perfect CSI (1/2)
Ergodic achievable uplink rate of the kth user
Proposition 1: Assume that the BS has perfect CSI and the transmit power of each user is scaled with Mt according to , where Eu is fixed. Then,
  Massive MIMO effect
    Small-scale fading/ Inter-user interference goes away in the limit

## Slide 32: Massive MIMO Uplink Channel : Uplink Power Efficiency – Perfect CSI (2/2)
Uplink performance with MRC – Perfect CSI
Capacity lower bound
Limit case
  Small-scale fading/ Inter-user interference goes away in the limit !
  Tx power can be scaled as
pu=Eu/M

## Slide 33: Massive MIMO Uplink Channel : Uplink Power Efficiency – Imperfect CSI (1/3)
Estimated CSI ( ) using MMSE channel estimation
Received signal vector after using the linear detector

## Slide 34: Massive MIMO Uplink Channel : Uplink Power Efficiency – Imperfect CSI (2/3)
Ergodic achievable uplink rate of the kth user
  If we cut the Tx power
   Both data and pilot signal suffer from the reduction in power.
   We cannot reduce power proportionally to 1/M.
Proposition 2: Assume that the BS has imperfect CSI, obtained by MMSE estimation from uplink pilots, and that the transmit power of each user is
, where Eu is fixed. Then,
Pilot power (pp)

## Slide 35: Massive MIMO Uplink Channel : Uplink Power Efficiency – Imperfect CSI (3/3)
Uplink performance with MRC – Imperfect CSI
Capacity lower bound
Limit case ( )
  Tx power can be scaled as
Squaring effect

## Slide 36: Massive MIMO Uplink Channel : Uplink Power Efficiency – Simulation Results
Required Power vs. M
  Simulation parameters
    K=10
    Target rate: 1bit/s/Hz
  Power scaling low
    Perfect CSI
    Imperfect CSI
  As M increases, the difference in performance between MRC and ZF (or MMSE) decreases.
    Perfect CSI: less than 1dB
    Imperfect CSI: less than 3dB
M↑  pu↓ as 1/M
Performance gap between
MRC and ZF (or MMSE)

## Slide 37: Multi-Cell Massive MIMO
Pilot Contamination & Inter-Cell Interference Problem

## Slide 38: Multi-Cell Massive MIMO : Inter-Cell Interference Problem (1/3)
Non-cooperative multi-cell environment
  Assumption: MRT precoder / 2 cell assumption
  MRT based transmit signal
    Transmit signal at BS 1:
    Transmit signal at BS 2:
  Received signal for R1

## Slide 39: Multi-Cell Massive MIMO : Inter-Cell Interference Problem (2/3)
 0

## Slide 40: Multi-Cell Massive MIMO : Inter-Cell Interference Problem (3/3)
0
0
1

## Slide 41: Multi-Cell Massive MIMO : Pilot Contamination Problem (1/5)
Practical problems for non-cooperative multi-cell
  Assumption [7]
    Non-cooperative multi-cell with TDD mode
    MIMO-OFDM system with MU-MIMO
  To perfectly mitigate interference at large M, exact MRT scheme is needed
  Perfect CSIT is necessary to design exact MRT precoder
    UL pilots are allocated in same time-frequency elements to obtain perfect CSIT
    UL pilots can be separated by orthogonal sequences  Can obtain perfect CSIT
  Problem: Exact same time-frequency elements with same pilot sequence
    Perfect CSIT is impossible  pilot contamination problem
  [7] F. Rusek et al., “Scailing up MIMO: Opportunities and challenges with very large arrays,”

## Slide 42: Multi-Cell Massive MIMO : Pilot Contamination Problem (2/5)

## Slide 43: Multi-Cell Massive MIMO : Pilot Contamination Problem (3/5)
SIR for 2-cell MU-MIMO with pilot contamination
  Received signal at R1
  Desired signal
  Interference signal
  Received SIR
No small scale fading effects
Pilot contamination is independent from pilot power

## Slide 44: Multi-Cell Massive MIMO : Pilot Contamination Problem (4/5)
SIR for multi-cell MU-MIMO with pilot contamination [7]
  MRT based SINR for l-th UE
  ZF-BF based SINR for l-th UE [7]
    If pp  0, MRT = ZF-BF
No small scale fading effects
Pilot contamination is independent from pilot power
No small scale fading effects
Pilot contamination is dependent from pilot power
  [7] F. Rusek et al., “Scailing up MIMO: Opportunities and challenges with very large arrays,”

## Slide 45: Multi-Cell Massive MIMO : Pilot Contamination Problem (5/5)
Simulation Results [7]
  SIR for MRT and ZF as function of M and K=10
Simulation Parameters
  MRT / ZF-BF is considered
  Number of users (K): 10
  Cell diameter: 1600m
  Large scale + small scale considered
  Performance is limited by pilot contamination
Conclusion from simulation results
  Finite M  MRT < ZF-BF
  Infinite M  MRT > ZF-BF
Finite M: ZF > MRT
Infinite M: ZF < MRT
  [7] F. Rusek et al., “Scailing up MIMO: Opportunities and challenges with very large arrays,”

## Slide 46: Homework
1. What are the advantages of Massive MIMO technology？
2. For a 100 x 4 Massive MIMO channel, when the transmit power Pd=10 dB, what is the capacity?
Tips: For Q1, see P5; For Q2, see P15